## Slide 1
Design Laboratory - II (ME306)
WAVE ENERGY CONVERTER CONTROL SYSTEM WITH VIBRATION AND MECHANICAL CONTROL
Presented By -
Ankur Singh (2022MEB1298)
Arnav Maitreya (2022MEB1299)
Akshat Srivastava (2022MEB1294)
Ainala Kannaiah (2022MEB1292)
Akshat Pathak (2022MEB1293)
Supervised by:
Jitendra Prasad Srikant Sekhar Padhee

## Slide 2
  To simulate and analyze a point-absorber Wave Energy Converter (WEC) for efficient wave energy harvesting.
  Implement a vibration-based control strategy using a PID controller to stabilize and enhance energy conversion.
  Employ machine learning to predict optimal PID values for maximum power generation.
  Validate system performance using Simulink and Simscape simulations.
OBJECTIVE

## Slide 3
  The project focuses on energy extraction from sinusoidal ocean waves using a mechanical oscillator.
  A PID controller is tuned to control the damping force, influencing the WEC’s displacement and velocity.
  ML is used to learn the relationship between PID parameters and resulting power output, enabling optimization.
  Data for ML training is obtained through systematic PID sweeps in simulation.
PROJECT OVERVIEW

## Slide 4
  WEC modeled as a mass-spring-damper system influenced by wave-induced sinusoidal forces.
  Control signal (from PID) adjusts damping characteristics dynamically.
  The system outputs include displacement, velocity, and instantaneous power.
  Power is computed as the product of force and velocity over time.
SYSTEM MODEL

## Slide 6
  Equation of Motion: mẍ + cẋ + kx = F(t),
  where F(t) = A sin(ωt)
  PID input: Error = desired − actual velocity
  PID output used to control damping coefficient in real-time
  Simulink block models created for: wave force input, dynamic system, PID loop, and power calculator
SIMULATION ARCHITECTURE

## Slide 7
SIMULATION WORKFLOW
Step 1: Assign physical parameters (mass, spring constant, damping)
Step 2: Implement wave input as a sinusoidal force function
Step 3: Use PID to dynamically adjust the damping
Step 4: Sweep 250 combinations of (Kp, Ki, Kd)
Step 5: Record power output for each set → dataset for ML model

## Slide 10
Fig Simulation results ( Power, Velocity , Position ) in ML tuned PID conditions , Kp =28 , Ki = 0 , Kd = 12 .

## Slide 12
MACHINE LEARNING MODEL
  Supervised learning approach using a feedforward neural network (FNN)
  Inputs: Kp, Ki, Kd values
  Output: Corresponding power output predicted
  Architecture: Dense layers with ReLU activations, MSE loss, and Adam optimizer
  Trained using the dataset generated from simulations

## Slide 13
TRAINING & OPTIMIZATION
  250 PID samples split into training and validation sets
  Early stopping used to prevent overfitting
  Once trained, model is used to evaluate 500,000 random PID sets
  PID combination with maximum predicted power selected as optimal

## Slide 14
LOSS CURVE

## Slide 15
OPTIMIZATION RESULTS
  Optimized PID values led to a predicted power output 12.5% higher than original tuned PID
  Simulation confirmed improved displacement tracking and increased velocity
  ML-based optimization significantly reduced manual trial-and-error tuning

## Slide 16
CONCLUSION
  Successfully integrated control system simulation with machine learning-based optimization
  Demonstrated a practical and scalable approach for improving WEC performance
  Framework is extendable to other renewable energy systems with dynamic parameters
  Future work: include wave variability, environmental damping, and real-time PID tuning